Symbolic
Execution

---
One-Slide Summary
- Verification Conditions make axiomatic semantics practical. We can compute verification conditions forward for use on unstructured code (= assembly language). This is sometimes called symbolic execution.
- We can add extra invariants or drop paths (dropping is unsound) to help verification condition generation scale.
- We can model exceptions, memory operations and data structures using verification condition generation.

---
Axiomatic Semantics III --- The Verification Crusade
Symbolic Execution

---
Not Quite Weakest Preconditions
Not Quite Weakest Preconditions
Recall what we are trying to do:
)
false
true
Pre(s, B)
weak
strong
weakest
precondition: WP(c, B)
A
Construct a verification condition: VC(c, B)
Our loops will be annotated with loop invariants!
VC is guaranteed to be stronger than WP
But still weaker than A: A ) VC(c, B) ) WP(c, B)
verification
condition: VC(c, B)

---
Groundwork
Groundwork
Factor out the hard work
  - Loop invariants
  - Function specifications (pre- and post-conditions)
- Assume programs are annotated with such specs
  - Good software engineering practice anyway
  - Requiring annotations = Kiss of Death?
- New form of while that includes a loop invariant:
whileInv b do c
  - Invariant formula Inv must hold every time before b is evaluated
- A process for computing VC(annotated_command, post_condition) is called VCGen

---
Verification Condition Generation
Verification Condition Generation
Mostly follows the definition of the wp function:
VC(skip, B)	= B
VC(c1; c2, B)	= VC(c1, VC(c2, B))
VC(if b then c1 else c2, B)	=
b ) VC(c1, B) Æ :b ) VC(c2, B)
VC(x := e, B)	= [e/x] B
VC(let x = e in c, B)	= [e/x] VC(c, B)
VC(whileInv b do c, B)	= ?

---
VCGen for WHILE
VCGen for WHILE
     VC(whileInv e do c, B) =
Inv Æ (8x1…xn. Inv ) (e ) VC(c, Inv) Æ : e ) B) )
- Inv is the loop invariant (provided externally)
- x1, …, xn are all the variables modified in c
The 8 is similar to the 8 in mathematical induction:
P(0) Æ 8n 2 N. P(n) ) P(n+1)
Inv holds
on entry
B holds when the
loop terminates
in an arbitrary iteration
Inv is preserved in
an arbitrary iteration

---
Example VCGen Problem
Example VCGen Problem
Let’s compute the VC of this program with respect to post-condition x  0
x = 0;
y = 2;
whilex+y=2 y > 0 do
    y := y - 1;
    x := x + 1
First, what do we expect? What pre-condition do we need to ensure x0 after this?

---
Example of VC
Example of VC
By the sequencing rule, first we do the while loop (call it w):
whilex+y=2 y > 0 do
   y := y - 1;
   x := x + 1
VCGen(w, x  0) = x+y=2 Æ
8x,y. x+y=2 ) (y>0 ) VC(c, x+y=2) Æ y·0 ) x  0)
VCGen(y:=y-1 ; x:=x+1, x+y=2) =
  (x+1) + (y-1) = 2
w Result: x+y=2 Æ
8x,y. x+y=2 ) (y>0 ) (x+1)+(y-1)=2 Æ y·0 ) x  0)
Preserve loop invariant
Ensure post on exit

---
Example of VC (2)
Example of VC (2)
VC(w, x  0) = x+y=2 Æ
8x,y. x+y=2 )
(y>0 ) (x+1)+(y-1)=2 Æ y·0 ) x  0)
VC(x := 0; y := 2 ; w, x  0) = 0+2=2 Æ
8x,y. x+y=2 )
(y>0 ) (x+1)+(y-1)=2 Æ y·0 ) x  0)
So now we ask an automated theorem prover to prove it.

---
Thoreau, Thoreau, Thoreau
Thoreau, Thoreau, Thoreau
$ ./Simplify
> (AND (EQ (+ 0 2) 2)
(FORALL ( x y ) (IMPLIES (EQ (+ x y) 2)
(AND (IMPLIES (> y 0)
(EQ (+ (+ x 1)(- y 1)) 2))
(IMPLIES (<= y 0) (NEQ x 0))))))
1: Valid.
- Huzzah!
- Simplify is a non-trivial five megabytes
- Z3 is 15+ megabytes

---
Can We Mess Up VCGen?
Can We Mess Up VCGen?
- The invariant is from the user (= the adversary, the untrusted code base)
- Let’s use a loop invariant that is too weak, like “true”.
- VC = true Æ	8x,y. true )
        (y>0 ) true Æ y·0 ) x  0)
- Let’s use a loop invariant that is false, like “x  0”.
- VC = 0  0 Æ	8x,y. x  0 )
        (y>0 ) x+1  0 Æ y·0 ) x  0)

---
Emerson, Emerson, Emerson
Emerson, Emerson, Emerson
$ ./Simplify
> (AND TRUE
  (FORALL ( x y ) (IMPLIES TRUE
    (AND (IMPLIES (> y 0) TRUE)
        (IMPLIES (<= y 0) (NEQ x 0))))))
Counterexample: context:
    (AND
      (EQ x 0)
      (<= y 0)
    )
1: Invalid.
OK, so we won’t be fooled.

---
Soundness of VCGen
Soundness of VCGen
Simple form
² { VC(c,B) } c { B }
Or equivalently that
² VC(c, B) ) wp(c, B)
- Proof is by induction on the structure of c
  - Try it!
- Soundness holds for any choice of invariant!
- Next: extensions to Symbolic Execution

---
Where Are We?
Where Are We?
Axiomatic Semantics: the meaning of a program is what is true after it executes
Hoare Triples: {A} c {B}
Weakest Precondition: { WP(c,B) } c {B}
Verification Condition: A)VC(c,B))WP(c,b)
  - Requires Loop Invariants
  - Backward VC works for structured programs
  - Here we are today …
  - Forward VC (Symbolic Exec) works for assembly

---
Today’s Cunning Plan
- Symbolic Execution & Forward VCGen
- Handling Exponential Blowup
  - Invariants
  - Dropping Paths
- VCGen For Exceptions	(double trouble)
- VCGen For Memory	(McCarthyism)
- VCGen For Structures	(have a field day)
- VCGen For “Dictator For Life”

---
VC and Invariants
VC and Invariants
Consider the Hoare triple:
{x  0} whileI(x) x  5 do x := x + 1 {x = 6}
The VC for this is:
x  0  I(x)  x. (I(x)  (x > 5  x = 6 
        x  5  I(x+1) ))
- Requirements on the invariant:
  - Holds on entry	x. x  0  I(x)
  - Preserved by the body	x. I(x)  x  5  I(x+1)
  - Useful	x. I(x)  x > 5  x = 6
- Check that I(x) = x  6 satisfies all constraints

---
Forward VCGen
Forward VCGen
- Traditionally the VC is computed backwards
  - That’s how we’ve been doing it in class
  - Backwards works well for structured code
- But it can also be computed forward
  - Works even for un-structured languages (e.g., assembly language)
  - Uses symbolic execution, a technique that has broad applications in program analysis
    - e.g., the PREfix tool (Intrinsa, Microsoft) does this
    - Test input generation, document generation, specification mining, security analyses, ...

---
Forward VC Gen Intuition
Forward VC Gen Intuition
Consider the sequence of assignments
x1 := e1; x2 := e2
The VC(c, B) = [e1/x1]([e2/x2]B)
        = [e1/x1, e2[e1/x1]/x2] B
- We can compute the substitution in a forward way using symbolic execution (aka symbolic evaluation)
  - Keep a symbolic state that maps variables to expressions
  - Initially, 0 = { }
  - After x1 := e1, 1 = { x1 ! e1 }
  - After x2 := e2, 2 = {x1 ! e1, x2 ! e2[e1/x1] }
  - Note that we have applied 1 as a substitution to right-hand side of assignment x2 := e2

---
Simple Assembly Language
Simple Assembly Language
Consider the language of instructions:
I ::=	x := e | f() | if e goto L | goto L |
L: | return | inv e
- The “inv e” instruction is an annotation
  - Says that boolean expression e is true at that point
- Each function f() comes with Pref and Postf annotations (pre- and post-conditions)
- New Notation (yay!): Ik is the instruction at address k

---
Symex States
Symex States
We set up a symbolic execution state:
  : Var ! SymbolicExpressions
 (x) = the symbolic value of x in state 
 [x:=e] = a new state in which x’s value is e
We use states as substitutions:
(e) - obtained from e by replacing x with (x)
Much like the opsem so far …

---
Symex Invariants
Symex Invariants
- The symbolic executor tracks invariants passed
- A new part of symex state: Inv µ {1…n}
- If k 2 Inv then Ik is an invariant instruction that we have already executed
- Basic idea: execute an inv instruction only twice:
  - The first time it is encountered
  - Once more time around an arbitrary iteration

---
Symex Rules
Symex Rules
Define a VC function as an interpreter:
VC : Address £ SymbolicState £ InvariantState ! Assertion
Recall: Inv =
“invariants
visited so far”
if Ik = return
(Postcurrent-function)
if Ik = x := e
VC(k+1, [x:=(e)], Inv)
VC(k, , Inv) =
if Ik = f()
(Pref) Æ
8a1..am.’(Postf) )
     VC(k+1, ’, Inv)
(where y1, …, ym are modified by f)
and a1, …, am are fresh parameters
and ’ = [y1 := a1, …, ym := am]
if Ik = if e goto L
   e ) VC(L, , Inv) Æ
: e ) VC(k+1, , Inv)
if Ik = goto L
VC(L, , Inv)

---
Symex Invariants (2a)
Symex Invariants (2a)
Two cases when seeing an invariant instruction:
1. We see the invariant for the first time
  - Ik = inv e
  - k  Inv (= “not in the set of invariants we’ve seen”)
  - Let {y1, …, ym} = the variables that could be modified on a path from the invariant back to itself
  - Let a1, …, am be fresh new symbolic parameters
VC(k, , Inv) =
        (e) Æ 8a1…am. ’(e) ) VC(k+1, ’, Inv [ {k}])
 with ’ = [y1 := a1, …, ym := am]
        (like a function call)

---
Symex Invariants (2b)
Symex Invariants (2b)
We see the invariant for the second time
  - Ik = inv E
  - k 2 Inv
VC(k, , Inv) = (e)
        (like a function return)
Some tools take a more simplistic approach
  - Do not require invariants
  - Iterate through the loop a fixed number of times
  - PREfix, versions of ESC (DEC/Compaq/HP SRC)
  - Sacrifice completeness for usability

---
Symex Summary
Symex Summary
  - Let x1, …, xn be all the variables and a1, …, an fresh parameters
  - Let 0 be the state [x1 := a1, …,xn :=an]
  - Let ; be the empty Inv set
For all functions f in your program, prove:
        8a1…an. 0(Pref) ) VC(fentry, 0, )
- If you start the program by invoking any f in a state that satisfies Pref, then the program will execute such that
  - At all “inv e” the e holds, and
  - If the function returns then Postf holds
- Can be proved w.r.t. a real interpreter (operational semantics)
- Or via a proof technique called co-induction (or, assume-guarantee)

---
Forward VCGen Example
Forward VCGen Example
Consider the program
        Precondition: x · 0
Loop: inv x · 6
        if x > 5 goto End
        x := x + 1
        goto Loop
End: return Postconditon: x = 6

---
Forward VCGen Example (2)
Forward VCGen Example (2)
 8x.
        x · 0 )
        x · 6 Æ
        8x’.
        (x’ · 6 )
        x’ > 5 ) x’ = 6
        Æ
        x’ · 5 ) x’ + 1 · 6 )
VC contains both proof obligations and assumptions about the control flow

---
VCs Can Be Large
VCs Can Be Large
Consider the sequence of conditionals
(if x < 0 then x := - x); (if x  3 then x += 3)
  - With the postcondition P(x)
- The VC is
x < 0 Æ -x  3	 P(-x + 3)	Æ
x < 0 Æ -x > 3	 P(-x)	Æ
x  0 Æ x  3	 P(x + 3)	Æ
x  0 Æ x > 3	 P(x )
There is one conjunct for each path
) exponential number of paths!
  - Conjuncts for infeasible paths have un-satisfiable guards!
- Try with P(x) = x  3

---
English Prose
341. Van and Hitomi walked an inaudible distance from those guy's Van was hanging out with.
253. However, when he got into his chamber and sat down with a blank canvas propped up on its easel, his vision vanished as if it were nothing but a floating dust moat.
352. "Good evening my league." He picked her up by the wrist. "I think that you and I have some talking to do, actually I have a preposition"

---
Computer Science
This American Turing award winner is known for the “law” that “Adding humans to a late software project makes it later.” The Turing Award citation notes landmark contributions to operating systems, software engineering and computer architecture. Notable works include No Silver Bullet: Essence and Accidents of Software Engineering and The ___ ___ ___.

---
Q:  Theatre  (019 / 842)
Q: Theatre (019 / 842)
Name the composer or the title of the 1937 musical that includes the lyrics: "O Fortuna, velut luna statu variabilis, semper crescis aut decrescis; vita detestabilis nunc obdurat et tunc curat ludo mentis aciem, egestatem, potestatem dissolvit ut glaciem."

---
VCs Can Be Exponential
VCs Can Be Exponential
- VCs are exponential in the size of the source because they attempt relative completeness:
  - Perhaps the correctness of the program must be argued independently for each path
- Unlikely that the programmer wrote a program by considering an exponential number of cases
  - But possible. Any examples? Any solutions?

---
VCs Can Be Exponential
- VCs are exponential in the size of the source because they attempt relative completeness:
  - Perhaps the correctness of the program must be argued independently for each path
Standard Solutions:
  - Allow invariants even in straight-line code
  - And thus do not consider all paths independently!

---
Invariants in Straight-Line Code
Invariants in Straight-Line Code
- Purpose: modularize the verification task
- Add the command “after c establish Inv”
  - Same semantics as c (Inv is only for VC purposes)
    VC(after c establish Inv, P) =def
VC(c,Inv)  xi. Inv  P
    - where xi are the ModifiedVars(c)
- Use when c contains many paths
after if x < 0 then x := - x establish x  0;
if x  3 then x += 3 { P(x) }
VC is now:
(x < 0  - x  0) Æ (x  0  x  0) Æ
x. x  0  (x  3  P(x+3) Æ x > 3  P(x))

---
Dropping Paths
Dropping Paths
- In absence of annotations, we can drop some paths
- VC(if E then c1 else c2, P) = choose one of
  - E  VC(c1, P)  E  VC(c2, P)	(drop no paths)
  - E  VC(c1, P)	(drops “else” path!)
  - E  VC(c2, P)	(drops “then” path!)
We sacrifice soundness! (we are now unsound)
  - No more guarantees
  - Possibly still a good debugging aid
- Remarks:
  - A recent trend is to sacrifice soundness to increase usability (e.g., Metal, ESP, even ESC)
  - The PREfix tool considers only 50 non-cyclic paths through a function (almost at random)

---
VCGen for Exceptions
VCGen for Exceptions
We extend the source language with exceptions without arguments (cf. HW2):
  - throw	throws an exception
  - try c1 catch c2	executes c2 if c1 throws
- Problem:
  - We have non-local transfer of control
  - What is VC(throw, P) ?

---
VCGen for Exceptions
We extend the source language with exceptions without arguments (cf. HW2):
  - throw	throws an exception
  - try c1 catch c2	executes c2 if c1 throws
- Problem:
  - We have non-local transfer of control
  - What is VC(throw, P) ?
- Standard Solution: use 2 postconditions
  - One for normal termination
  - One for exceptional termination

---
VCGen for Exceptions (2)
VCGen for Exceptions (2)
VC(c, P, Q) is a precondition that makes c either not terminate, or terminate normally with P or throw an exception with Q
Rules
VC(skip, P, Q)	= P
VC(c1; c2, P, Q)	= VC(c1, VC(c2, P, Q), Q)
VC(throw, P, Q)	= Q
VC(try c1 catch c2, P, Q)	= VC(c1, P, VC(c2, P, Q))
VC(try c1 finally c2, P, Q)	= ?

---
VCGen Finally
VCGen Finally
Given these:
VC(c1; c2, P, Q) = VC(c1, VC(c2, P, Q), Q)
VC(try c1 catch c2, P, Q) = VC(c1, P, VC(c2, P, Q))
Finally is somewhat like “if”:
VC(try c1 finally c2, P, Q) =
VC(c1, VC(c2, P, Q), true)	Æ
 VC(c1, true, VC(c2, Q, Q))
Which reduces to:
VC(c1, VC(c2, P, Q), VC(c2, Q, Q))

---
Hoare Rules and the Heap
Hoare Rules and the Heap
When is the following Hoare triple valid?
        { A } *x := 5 { *x + *y = 10 }
A should be “*y = 5 or x = y”
The Hoare rule for assignment would give us:
  - [5/*x](*x + *y = 10) = 5 + *y = 10 =
  - *y = 5 (we lost one case)
Why didn’t this work?

---
Handling The Heap
Handling The Heap
- We do not yet have a way to talk about memory (the heap, pointers) in assertions
- Model the state of memory as a symbolic mapping from addresses to values:
  - If A denotes an address and M is a memory state then:
  - sel(M,A) denotes the contents of the memory cell
  - upd(M,A,V) denotes a new memory state obtained from M by writing V at address A

---
More on Memory
More on Memory
- We allow variables to range over memory states
  - We can quantify over all possible memory states
- Use the special pseudo-variable  (mu) in assertions to refer to the current memory
- Example:
i. i  0  i < 5  sel(, A + i) > 0
says that entries 0..4 in array A are positive

---
Hoare Rules: Side-Effects
Hoare Rules: Side-Effects
- To model writes we use memory expressions
  - A memory write changes the value of memory
Important technique: treat memory as a whole
And reason later about memory expressions with inference rules such as (McCarthy Axioms, ~‘67):
{ B[upd(, A, E)/] } *A := E {B}
if A1  A2
V
if A1  A2
sel(M, A2)
sel(upd(M, A1, V), A2) =

---
Memory Aliasing
Memory Aliasing
- Consider again: { A } *x := 5 { *x + *y = 10 }
- We obtain:
     A = [upd(, x, 5)/] (*x + *y = 10)
        = [upd(, x, 5)/] (sel(, x) + sel(, y) = 10)
(1) = sel(upd(, x, 5), x) + sel(upd(, x, 5), y) = 10
        = 5 + sel(upd(, x, 5), y) = 10
        = if x = y then 5 + 5 = 10 else 5 + sel(, y) = 10
(2) = x = y or *y = 5
- Up to (1) is theorem generation
- From (1) to (2) is theorem proving

---
Alternative Handling for Memory
Alternative Handling for Memory
- Reasoning about aliasing can be expensive
  - It is NP-hard (and/or undecideable)
- Sometimes completeness is sacrificed with the following (approximate) rule:
The meaning of “obviously” varies:
The addresses of two distinct globals are 
The address of a global and one of a local are 
PREfix and GCC use such schemes
otherwise (p is a fresh new parameter)
P
if A1 (obviously) A2
V
if A1  (obviously) A2
sel(M, A2)
sel(upd(M, A1, V), A2) =

---
VCGen Overarching Example
VCGen Overarching Example
- Consider the program
  - Precondition: B : bool  A : array(bool, L)
1: I := 0
    R := B
3: inv I  0  R : bool
    if I  L goto 9
    assert saferd(A + I)
    T := *(A + I)
    I := I + 1
    R := T
    goto 3
9: return R
  - Postcondition: R : bool

---
VCGen Overarching Example
 8A. 8B. 8L. 8
        B : bool Æ A : array(bool, L) )
        0 ¸ 0 Æ B : bool Æ
        8I. 8R.
        I ¸ 0 Æ R : bool )
        I ¸ L ) R : bool
        Æ
        I < L ) saferd(A + I) Æ
        I + 1 ¸ 0 Æ
        sel(, A + I) : bool
VC contains both proof obligations and assumptions about the control flow

---
Mutable Records - Two Models
Mutable Records - Two Models
- Let r : RECORD { f1 : T1; f2 : T2 } END
- For us, records are reference types
- Method 1: one “memory” for each record
  - One index constant for each field
  - r.f1 is sel(r,f1) and r.f1 := E is r := upd(r,f1,E)
- Method 2: one “memory” for each field
  - The record address is the index
  - r.f1 is sel(f1,r) and r.f1 := E is f1 := upd(f1,r,E)
Only works in strongly-typed languages like Java
  - Fails in C where &r.f2 = &r + sizeof(T1)

---
VC as a “Semantic Checksum”
VC as a “Semantic Checksum”
- Weakest preconditions are an expression of the program’s semantics:
  - Two equivalent programs have logically equivalent WPs
  - No matter how different their syntax is!
VC are almost as powerful

---
VC as a “Semantic Checksum” (2)
VC as a “Semantic Checksum” (2)
Consider the “assembly language” program to the right
x := 4
x := (x == 5)
   assert x : bool
x := not x
   assert x
High-level type checking is not appropriate here
The VC is: ((4 == 5) : bool)  (not (4 == 5))
No confusion from reuse of x with different types

---
Invariance of VC Across Optimizations
Invariance of VC Across Optimizations
- VC is so good at abstracting syntactic details that it is syntactically preserved by many common optimizations
  - Register allocation, instruction scheduling
  - Common subexp elim, constant and copy propagation
  - Dead code elimination
- We have identical VCs whether or not an optimization has been performed
  - Preserves syntactic form, not just semantic meaning!
- This can be used to verify correctness of compiler optimizations (Translation Validation)

---
VC Characterize a Safe Interpreter
VC Characterize a Safe Interpreter
- Consider a fictitious “safe” interpreter
  - As it goes along it performs checks (e.g. “safe to read from this memory addr”, “this is a null-terminated string”, “I have not already acquired this lock”)
  - Some of these would actually be hard to implement
- The VC describes all of the checks to be performed
  - Along with their context (assumptions from conditionals)
  - Invariants and pre/postconditions are used to obtain a finite expression (through induction)
VC is valid ) interpreter never fails
  - We enforce same level of “correctness”
  - But better (static + more powerful checks)

---
VC Big Picture
VC Big Picture
Verification conditions
  - Capture the semantics of code + specifications
  - Language independent
  - Can be computed backward/forward on structured/unstructured code
  - Make Axiomatic Semantics practical

---
Invariants Are Not Easy
Invariants Are Not Easy
Consider the following code from QuickSort
int partition(int *a, int L0, int H0, int pivot) {
     int L = L0, H = H0;
     while(L < H) {
        while(a[L] < pivot) L ++;
        while(a[H] > pivot) H --;
        if(L < H) { swap a[L] and a[H] }
    }
    return L
}
- Consider verifying only memory safety
- What is the loop invariant for the outer loop ?

---
Done!
Questions?